## Slide 1: EEL 4436C/5437C Microwave Engineering
Prof. Xun Gong
Lecture 2 – Transmission Line

## Slide 2: Two-Wire Line
Wire radius = a
Wire spacing = S
a<<S
Z0 > 100Ω
Z0 ~ 300Ω
Used mostly in TV applications to connect to “Rabbit-Ear” dipole antenna
Suffers from radiation Loss at f > 300 MHz

## Slide 3: Coax Line
Z0=75Ω (TV)
Z0=50Ω (RF/MW system)
The most common T. Line for connecting components. Have virtually replaced waveguide except for high-power (>1 KW) applications

## Slide 4: Why 50 Ohm?
characteristic impedance
for coaxial airlines (ohms)
10
20
30
40
50
60
70
80
90
100
1.0
0.8
0.7
0.6
0.5
0.9
1.5
1.4
1.3
1.2
1.1
normalized values
50 ohm standard
attenuation is lowest at 77 ohms
power handling capacity peaks at 30 ohms

## Slide 5: Coax Connector
Mode free up 18 GHz
Slot in outer conductor < 12 GHz
UHF
< 100 MHz (UHF: 30-300 MHz)
Cheap but outdated
BNC
Mode free up to 18 GHz
Practically used up to 3-4 GHz
TNC
Improved from BNC
Practically used up to 11-12 GHz
Some can go up to 18 GHz

## Slide 6: Coax Connector
SMA
With semi-rigid cable up to 18 GHz
Otherwise < 12 GHz
Torque wrench required (5 in-lb)
Smaller and cheaper than SMA
Work up to 10 GHz
SMC
Push on and off
Work up to 4 GHz
MCX
MMCX
For wireless, GPS, cell phone
Very small, snap on/off
Work up to 6 GHz

## Slide 7: Instrument Connector
APC7
For repeated connections
Up to 18 GHz
Torque wrench required (12 in-lb)
3.5mm (<26.5 GHz)
2.92 mm or K connector (<40 GHz)
2.4mm (<50 GHz)
1.85 mm or V connector (<65 GHz)
1.0 mm (< 110GHz)
All air dielectric, torque of 8 in-lb except for 1.0 mm (3 in-lb)
3.5mm, 2.92 mm, and SMA are physically compatible. But SMA quality is not that good. So you need a connector saver!

## Slide 8: Microstrip Line
Wide Lines -> Large C/Unit Length-> Low impedance
Narrow Lines -> Small C/Unit Length-> High impedance
Wide Lines -> Small Resistance -> Low Loss
Narrow Lines -> Large Resistance -> High Loss
Wide Lines -> fields mostly in dielectric -> (εeff -> εr)
Narrow Lines -> a lot of fields in air -> (εeff -> (εr+1)/2)
Analytic formulas for calculating εeff , Z0 are in Pozar’s book

## Slide 9: Microstrip Line
H < λg/15 before radiation occurs in the substrate
Typical H (λg/30 to λg/15)
Less H -> less W for the same Z0
Reduce circuit size but induce more loss
In RF applications, H ~ λg/100 to result in compact circuits

## Slide 10: Coplanar Waveguide
CPW without Ground Plane
CPW with Ground Plane
Coax-CPW Transition
CPW based Mixer

## Slide 11: Coplanar Waveguide
Larger a -> Lower impedance
Larger b-a (larger gap) -> Higher impedance
Larger h -> The less dependence of Z0 on h
Larger ε -> Lower impedance
Use ADS LineCal to calculate all the properties of CPW

## Slide 12: Other T. Lines
Slot Line for Vivaldi Antenna
Strip Line (TEM)
No radiation loss, for millimeter-wave applications

## Slide 13: Transitions
SMA to CPW Transition
SMA to Microstrip Transition

## Slide 14: T. Line Components
Five-Pole (Resonator) Hairpin Filter
4-Way Power Combiner/Splitter
Branch line Hybrid
Ring (Rat Race) Hybrid

## Slide 15: T. Line Component
Directional Coupler
Lange Coupler
Patch Antenna Array
Microwave Amplifier with Bias & Matching Networks

## Slide 16: T. Line Component
Attenuator
Attenuate signals to protect instruments
Isolator
Ferrite-based device, one-way traffic
Circulator
Ferrite-based 3-port device
DC Block
Block DC, Pass RF
Power Divider/Combiner