## Slide 1: Outline
Microstrip Line
Coplanar Waveguide (CPW)
General Solution for TE, TM, and TEM Waves
TEM Waves
TE Waves
TM Waves
Parallel Plate Waveguide
Rectangular Waveguide
Coaxial Line

## Slide 2
Microstrip Line
Hair pin bandpass filter
Directional Coupler
Low Noise Amplifier
Low pass filter

## Slide 3
Microstrip Line
Wide Lines  Large C/Unit Length  Low impedance
Narrow Lines  Small C/Unit Length High impedance
Wide Lines  Small Resistance  Low Loss
Narrow Lines  Large Resistance  High Loss
Wide Lines  fields mostly in dielectric  (εeff  εr)
Narrow Lines  a lot of fields in air  (εeff  (εr+1)/2)

## Slide 4
Microstrip Line
H < λg/15 before radiation occurs in the substrate  Typical H (λg/30  λg/15)
Less H  less W for the same Z0
Reduce circuit size but induce more loss
In RF applications, H ~ λg/100 to result in compact circuits
Use ADS LineCal/HFSS to calculate all the properties of Microstrip line
Analytic formulas for calculating εeff , Z0 are in Pozar’s book

## Slide 5
Coplanar Waveguide (CPW)
Cheng P. Wen is the inventor of Coplanar Waveguide in 1969, when working at RCA's Sarnoff Laboratories. The initial paper he published was: "Coplanar Waveguide: a surface strip transmission line suitable for nonreciprocal gyromagnetic device applications".
SP6T MEMS Switch

## Slide 6
Coplanar Waveguide (CPW)
Larger a  Lower impedance
Larger b-a (larger gap)  Higher impedance
Larger h  Less dependence of Z0 on h
Larger ε  Lower impedance

## Slide 7: General Solutions for TE, TM, and TEM
Assume the wave is propagating in +z direction.
Assume the wave is propagating in source-free regions (no charge, no current)

## Slide 8
General Solutions for TE, TM, and TEM

## Slide 9
TEM Waves (Ez = Hz = 0)
Only if
TEM waves can exist
The transverse fields of a TEM wave are identical to the static fields that can exist between conductors.

## Slide 10
TEM Waves
Therefore we can use the method in electric static fields
With boundary conditions, we can find the voltage at any location in the transverse plane.
The E field can be derived using:
The H field can be derived using:

## Slide 11
TEM Waves
In order to support TEM waves, at least two separate conductors are necessary.

## Slide 12
TE Waves (Ez = 0)
To solve for all field components, Hz needs to be found first:
since

## Slide 13
TM Waves (Hz = 0)
To solve for all field components, Ez needs to be found first:
since
Both TE and TM waves can be supported inside closed conductors.

## Slide 14
Parallel Plate Waveguide - TEM
Solve for the voltage with the given B.C.
E Field can be found:
H Field can be found:
You have already simulated the vector fields using HFSS
V =V0
V =0
y
x
d
W

## Slide 15
Parallel Plate Waveguide - TEM
V =V0
V =0
y
x
d
W

## Slide 16
Parallel Plate Waveguide - TM
B.C.
y
x
d
W
Cutoff frequency is determined by

## Slide 17
Parallel Plate Waveguide - TM
y
x
d
W
Do your homework: plot the vector field distribution using HFSS
Bouncing plane wave interpretation:
k
e
h
k
e
h
z
y

## Slide 18
Parallel Plate Waveguide - TE
B.C.
y
x
d
W
Cutoff frequency is determined by

## Slide 19
Parallel Plate Waveguide - TE
y
x
d
W
Do your homework: plot the vector field distribution using HFSS
Bouncing plane wave interpretation:
k
h
e
k
h
e
z
y

## Slide 20
Rectangular Waveguide - TE
y
x
b
a
Separation of Variables

## Slide 21
Rectangular Waveguide - TE
y
x
b
a
Boundary Conditions:
0
0
m, n cannot be 0 at the same time

## Slide 22
Rectangular Waveguide - TE
y
x
b
a

## Slide 23
Rectangular Waveguide – TE10

## Slide 24
Rectangular Waveguide – TE10

## Slide 25
Rectangular Waveguide – TE10
Waveguide slotted line
Surface Current
slotted Waveguide antenna

## Slide 26
Rectangular Waveguide – TE20

## Slide 27
Rectangular Waveguide – TE01

## Slide 28
Rectangular Waveguide – TE11

## Slide 29
Rectangular Waveguide - TM
y
x
b
a
Separation of Variables

## Slide 30
Rectangular Waveguide - TM
y
x
b
a
Boundary Conditions:
0
0
m, n cannot be 0

## Slide 31
Rectangular Waveguide - TM
y
x
b
a

## Slide 32
Rectangular Waveguide – TM11

## Slide 33
Rectangular Waveguide Modes
Mode | m | n | fc (GHz)
TE | 1 | 0 | 6.56
TE | 2 | 0 | 13.12
TE | 0 | 1 | 14.76
TM,TE | 1 | 1 | 16.156
X band Waveguide: a= 22.86 mm , b= 10.16 mm
Working frequency is between 6.56 and 13.12 GHz for single mode Operation

## Slide 34
Coaxial Line

## Slide 35
Coaxial Line - TEM
Laplace Equation for voltage:
Separation of Variables

## Slide 36
Coaxial Line - TEM
Since the voltage is constant for different angles, n = 0
Therefore,
Since

## Slide 37
Coaxial Line - TEM

## Slide 38
Coaxial Line – Higher-Order Modes
Coaxial lines support TEM, TE, and TM modes
Usually coaxial lines operate in single mode condition TEM
It is important to know the cutoff frequencies of higher-order modes
TE11 is the first higher-order mode
For TE modes, Ez = 0
B.C.

## Slide 39
Coaxial Line – Higher-Order Modes
Transcendental
When n = 1