## Slide 1: Outline
Impedance Matching
Single Stub Matching
Matching With Lumped Elements
Quarter Wavelength Transformer
Theory of Small Reflections
Multi-Sectional Transformer
Tapered Line
Bode-Fano Criterion

## Slide 2: Impedance Matching
Max. power transfer condition

## Slide 3: Single Stub Matching
One of the most common matching techniques at f > 3 GHz
Very low loss and does not occupy a lot of space on the circuit
Short (open) stub can only result in a reactive element

## Slide 4: Single Stub Matching
Zl =60 – j80(Ω)
Z0 =50 (Ω)
zl =1.2 – j1.6
yl =0.3 + j0.4
d1
d2
y1
y2
d1 =0.176-0.065=0.110λ
d2 =0.325-0.065=0.260λ
y1 =1+j1.47
y2 =1-j1.47
l1
l1 =0.095λ
l2
l2 =0.405λ

## Slide 5: Single Stub Matching
A 12-W GaN-HEMT power amplifier for Ku-band satellite communication

## Slide 6: Lumped Element Matching
Used extensively at low frequencies (300 MHz – 3 GHz)
Use Inductor/Capacitor to match any impedance
Case 1: series inductor (widely used in transistor matching)
Zl=1-jX
|Γ|=-10 dB
Allowable Zl

## Slide 7: Lumped Element Matching
Case 2: Shunt Capacitor
Yl=1-jB
Y chart
Z chart

## Slide 8: Lumped Element Matching
Case 3: Shunt Inductor
Case 4: Series Capacitor
Zl=1-jX
Yl=1-jB
The range of matching is limited by using one component.

## Slide 9: Lumped Element Matching
In Ancient Chinese philosophy, yin and yang (/jɪn/ and /jɑːŋ, jæŋ/; Chinese: 陰陽 yīnyáng pronounced [ín jǎŋ], lit. "dark-light", "negative-positive") is a concept of dualism, describing how obviously opposite or contrary forces may actually be complementary, interconnected, and interdependent in the natural world, and how they may give rise to each other as they interrelate to one another.[1]

## Slide 10: Lumped Element Matching
Case 5: shunt capacitor first Series Inductor second
Zl
Z0
Z2=1-jX
Zl
Find Y2
Cross with Re(Yl) circle
Allowable Zl
Allowable Yl

## Slide 11: Lumped Element Matching
Case 6: Series Inductor first shunt capacitor second
Zl
Z0
Y2=1-jB
Zl
Find Z2
Cross with Re(Zl) circle
Allowable Yl
Allowable Zl

## Slide 12: Lumped Element Matching

## Slide 13: Lumped Element Matching

## Slide 14: Effects of Adding L and C

## Slide 15: Lumped Element Matching

## Slide 16: Lumped Element Matching
Case 5 & 6 together covers the whole smith chart
Q(inductor)<100 for off chip component
Q(indcutor)<20 for on chip component
Q(capacitor)<100 for Metal-insulator-metal capacitance

## Slide 17: Quarter Wavelength Transformer

## Slide 18: Bandwidth (BW) Considerations
0

## Slide 19: Bandwidth (BW) Considerations

## Slide 20: Bandwidth (BW) Considerations

## Slide 21: Theory of Small Reflections

## Slide 22: Theory of Small Reflections

## Slide 23: Multi-Section Transformer

## Slide 24: Multi-Section Transformer

## Slide 25: Multi-Section Transformer

## Slide 26: Multi-Section Transformer

## Slide 27: Multi-Section Transformer

## Slide 28: Multi-Section Transformer

## Slide 29: Multi-Section Transformer

## Slide 30: Multi-Section Transformer

## Slide 31: Multi-Section Transformer

## Slide 32: Multi-Section Transformer

## Slide 33: Multi-Section Transformer

## Slide 34: Multi-Section Transformer

## Slide 35: Multi-Section Transformer

## Slide 36: Multi-Section Transformer

## Slide 37: Multi-Section Transformer

## Slide 38: Tapered Lines

## Slide 39: Tapered Lines

## Slide 40: Bode-Fano Criterion
For a given load, wider bandwidth can be achieved only at the expenses of a higher Γm in the passband
Γm cannot be zero unless = 0. Thus, a perfect matching can only be achieved at a finite number of frequencies.

## Slide 41: Bode-Fano Criterion
For a parallel RC network,
Therefore, the Bode-Fano limit can be expressed as:
The higher the Q factor, the narrower the bandwidth.
The same conclusion applies to the other three cases.